## Slide 1: Implementation of Different types of Filters
By Narsepalli Pradyumna
1RV19EC106
Signal and Systems (18TE45)

## Slide 2: Total 4 types of filters can be generated with a second order Transfer function

## Slide 3: Equations related to all the four types of Filters
Low Pass series RLC Filter
High Pass series RLC Filter
In this project I’m using a second order RLC circuit to realize Filters. It indicates that there will be two poles and a maximum of two zeros

## Slide 5: Damping Factor It measures the rate of decrease of oscillations when the source is removed
D=1
D=0
D=0.5

## Slide 6
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=0
Transfer Function
As we can observe from the graphs obtained from the equation.
Damping factor directly defines the nature of the transfer function and for damping factor=0 gives a sinosodial output irrespective of the type of the Filter.
NOTE: This type of Functions are called Undamped

## Slide 7
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=0
S-Plane
As we can observe from the graphs obtained from the equation.
Damping factor directly affects the poles locations and their nature.
In the case of Damping factor=0, both the poles are imaginary in nature.
Zeroes are depended on the numerator, therefore except for Band-Stop, zeroes are always real in nature. Band-Stop may or may not be purely real.

## Slide 8
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=0
Bode-Plot
As we can observe from the graphs obtained from the equation.
When magnitude is near to 0 then those frequencies are rejected since the final outcome is in the form (approx. 0) x input, thereby giving an output of near zero.
Damping factor induces a peak at the selected frequency before moving with its selected nature.
NOTE: In these cases I have chosen a gain of magnitude 5.

## Slide 9
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=0.5
Transfer Function
As we can observe from the graphs obtained from the equation.
Damping factor directly defines the nature of the transfer function and for damping factor=0.5 gives a sinosodial output which degrades with time irrespective of the type of the Filter.
NOTE: This type of Functions are called Under damped

## Slide 10
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=0.5
S-Plane
As we can observe from the graphs obtained from the equation.
Damping factor directly affects the poles locations and their nature.
In the case of Damping factor=0.5, both the poles contain both real and imaginary parts.
Zeroes are depended on the numerator, therefore except for Band-Stop, zeroes are always real in nature. Band-Stop may or may not be purely real.

## Slide 11
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=0.5
Bode-Plot
As we can observe from the graphs obtained from the equation.
When magnitude is less than or equal to 0 then those frequencies are rejected.
NOTE: In these cases I have chosen a gain of magnitude 5.

## Slide 12
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=1
Transfer Function
As we can observe from the graphs obtained from the equation.
Damping factor directly defines the nature of the transfer function and for damping factor=1 gives an exponential output which degrades with time irrespective of the type of the Filter.
NOTE: This type of Functions are called Critically damped

## Slide 13
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=1
S-Plane
As we can observe from the graphs obtained from the equation.
Damping factor directly affects the poles locations and their nature.
In the case of Damping factor=1, both the poles contain real parts.
NOTE: From this point onwards poles cease to exist in imaginary axis.

## Slide 14
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=1
Bode-Plot
As we can observe from the graphs obtained from the equation.
When magnitude is less than or equal to 0 then those frequencies are rejected.
NOTE: In these cases I have chosen a gain of magnitude 5.

## Slide 15
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=1.5
Transfer Function
As we can observe from the graphs obtained from the equation.
Damping factor directly defines the nature of the transfer function and for damping factor=1 gives an exponential output which degrades with time irrespective of the type of the Filter.
NOTE: This type of Functions are called Critically damped

## Slide 16
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=1.5
S-Plane
As we can observe from the graphs obtained from the equation.
Damping factor directly affects the poles locations and their nature.
In the case of Damping factor=1.5, both the poles are real.
Zeroes are depended on the numerator, therefore except for Band-Stop, zeroes are always real in nature. Band-Stop may or may not be purely real.

## Slide 17
Low-Pass Filter
High-Pass Filter
Band-Pass Filter
Band-Stop Filter
Damping Factor=1.5
Bode-Plot
As we can observe from the graphs obtained from the equation.
When magnitude is less than or equal to 0 then those frequencies are rejected.
NOTE: In these cases I have chosen a gain of magnitude 5.

## Slide 18
 | 0 (UNDAMPED) | 0.5 (UNDER DAMPED) | 1 (CRITICALLY DAMPED) | 1.5 (OVER DAMPED)
Low-Pass | TF(Transfer Function) is sinosodial No zeroes required and present Two imaginary poles are present Phase change is -180 to 0 | TF starts as a sine and slowly tuns into exponential No zeroes required and present Two imaginary poles are present Phase change is -180 to 0 | TF is exponential No zeroes required and present Two imaginary poles are present Phase change is -180 to 0 | TF is exponential No zeroes required and present Two imaginary poles are present Phase change is -180 to 0
High-Pass | TF is sinosodial Two overlapping zeroes are present Two imaginary poles are present Phase change is 0 to 180 | TF starts as a sine and slowly tuns into exponential Two overlapping zeroes are present Two imaginary poles are present Phase change is 0 to 180 | TF is exponential Two overlapping zeroes are present Two imaginary poles are present Phase change is 0 to 180 | TF is exponential Two overlapping zeroes are present Two imaginary poles are present Phase change is 0 to 180
Band-Pass | TF is sinosodial Two non-overlapping zeroes are present Two imaginary poles are present Phase change is -90 to 90 | TF starts as a sine and slowly tuns into exponential Two non-overlapping zeroes are present Two imaginary poles are present Phase change is -90 to 90 | TF is exponential Two non-overlapping zeroes are present Two imaginary poles are present Phase change is -90 to 90 | TF is exponential Two non-overlapping zeroes are present Two imaginary poles are present Phase change is -90 to 90
Band-Stop | TF is sinosodial Two non-overlapping imaginary zeroes are present Two imaginary poles are present Phase change is -135 to 45 | TF starts as a sine and slowly tuns into exponential Two non-overlapping imaginary zeroes are present Two imaginary poles are present Phase change is -135 to 45 | TF is exponential Two non-overlapping imaginary zeroes are present Two imaginary poles are present Phase change is -135 to 45 | TF is exponential Two non-overlapping imaginary zeroes are present Two imaginary poles are present Phase change is -135 to 45
Filters
Damping Factor

## Slide 19: Thank You